To run the demo of serpint, follow these instructions....

The demo will show you the capability of serpint to control the GPIO pins over a serial port. Part 2 will also show you the same thing can be done over a network. The serial monitor that you run has NO GPIO library loaded, only a standard serial library.

You Will Need....

1. A Raspberry Pi with Screen and Keyboard
2. A way to check GPIO voltages (Voltimiter, LED)
3. Serpint (Download from github.com/602p/serpint)

For Part 2 Extension [OPTIONAL]

1. Another computer (running linux)
2. A connection between them, on the same network
3. Serpint on the other computer

PART 1
This tests the GPIO control functionality of serpint

1. On your raspberry pi.... Cd to the bin directory of the serpint folder
2. Run
   ./serpint gpiotoserial ttyS44 4444
3. Open a new tab/tty and run
   ./serpint monitor
4. In the monitor, enter your serial port as /dev/ttyS44
5. Attach a voltimeter or light to gpio pins 4 and ground [ see http://elinux.org/images/2/2a/GPIOs.png]
6. Press space in the monitor to toggle the power to pin 4
7. When done, press q to quit the monitor
8. Run
   ./serpint cleanup

PART 2 [OPTIONAL]
This tests the networking functionality of serpint

1. Do steps 1&2 of PART 1
2. Run
   ./serpint serialtosock ttyS44 4445
3. Make note of your raspberry pi's IP address (you can find this out by doing
   sudo ifconfig|grep “inet addr”
   (you’ll want the top one)) You’ll need this in step 5
4. On another (linux) computer, download serpint
5. Cd to the bin folder and run
   ./serpint socktoserial ttyS44 192.168.1.7 4445
   You will want to replace 192.168.1.7 with the IP address that you got in step 3
6. Do steps 3-7, but on the second computer
7. Run
   ./serpint cleanup
   on bolth machines