To run the demo of serpint, follow these instructions....

You Will Need....

1. A Raspberry Pi
2. A way to check GPIO voltages [OPTIONAL, but you wont know if its working]
3. A way to talk to your raspberry pi (screen, keyboard)
4. Serpint (Download from github.com/602p/serpint)

For Part 2 Extension [OPTIONAL]

1. Another computer (linux)
2. A connection between them, on the same network
3. Serpint on the other computer

PART 1
This tests the GPIO control functionality of serpint

1. On your raspberry pi.... Cd to the bin directory of the serpint folder
2. Run ./serpint gpiotoserial ttyS44 4444
3. Open a new tab/tty and run ./serpint monitor
4. In the monitor, enter your serial port as /dev/ttyS44
5. Attach a voltimeter/light to gpio pins 4 and ground [http://elinux.org/images/2/2a/GPIOs.png] [OPTIONAL]
6. Press space in the monitor to toggle the power to pin 4
7. When done, press q to quit the monitor
8. Run ./serpint cleanup

PART 2 [OPTIONAL]
This tests the networking functionality of serpint

1. Do steps 1&2 of PART 1
2. Run ./serpint serialtosock ttyS44 4445
3. Make note of your raspberry pi's IP address (you can find this out by doing sudo ifconfig|grep “inet addr” (you’ll want the top one))
4. On another (linux) computer, download serpint
5. Cd to the bin folder and run ./serpint socktoserial ttyS44 [here you type in your raspberry pi's IP address] 4445
6. Do steps 3-7, but on the second computer
7. Run ./serpint cleanup on bolt machines